# 12.12 INTRAVENOUS INFUSION OF MORPHINE SULFATE

CCT PARAMEDICS

- These procedures/interventions shall only be performed by paramedics with CCT-P (Critical Care Transport-Paramedic) training and designation.

### Patients shall be placed on cardiac and pulse oximetry monitors for duration of transport.

### A non-invasive blood pressure monitor device that will record and print out routine blood pressure reading every fifteen (15) minutes will be utilized.

### Signed transfer orders from the transferring physician must be obtained prior to transport and must provide for maintaining the Morphine Sulfate infusion during transport.

### If medication administration is interrupted (infiltration, accidental disconnection, malfunctioning pump, etc.) the CCT-P may restart the IV line as delineated in the transfer orders. Caution must be used to prevent inadvertent overdose of medication.

### The following parameters shall apply to all patients with pre-existing Morphine Sulfate infusions:

- Regulation of the infusion rate will occur within the parameters as defined by the transferring physician, but may be titrated to the individuals response during transport

- In cases of severe respiratory depression, sedation, confusion, hypotension, bradycardia, nausea and vomiting, the medication infusion will be discontinued and Naloxone, if indicated, may be administered as directed by your county of origin’s EMS protocol. Notify the base physician.

## CCT-Ps may not initiate Morphine Sulfate infusions.